## Slide 1
DASAR TELEKOMUNIKASI
Konsep Dasar 2G, 3G, dan 4G
Syarifah Muthia Putri, ST., MT

## Slide 2: Circuit Switching vs. Packet Switching
Circuit Switching
  Mostly used in the voice call.
  Whenever a call is being made, a dedicated logical link needs to be established.
  Network resource is allocated and reserved for the subscriber for entire duration of the call.
Packet Switching
  Mostly used in the Packet Data Connection.. . e.g. internet browsing
  Whenever an MS sends or receives data, data is organized into packet and each packet has source / destination ID.

## Slide 3: Core Network : GSM
The core network in GSM is basically the circuit core.
In GPRS, EDGE and UMTS, it has two components, the circuit core and the packet core, which are responsible for voice and data respectively.
In GSM, core or circuit-core network planning is also known as switch planning, because it is mainly related to the mobile switching centre (MSC), also called 'Switch'.
Core network planning in GSM consists of network elements such as MSC, VLR, HLR, AC and EIR.

## Slide 4: Core Network Planning : GSM

## Slide 5: Core Network : 3G
Core network planning of a third-generation (WCDMA) system consists of both circuit core and packet core planning.
The scope of core network planning includes dimensioning of network elements such as MOW, MSC (and VLR) and HLR (and AC/EIR) from the CS side, while the PS core will include SGSN, GGSN along with interfaces.

## Slide 6: Core Network : 3G

## Slide 7: 2G and 3G Network Architecture
User plane
Control plane
SGSN
GGSN
Packet Data Network
e..g Internet
Gi
Gn
IuPS
Gb
BSC
BTS
MS
Abis
RNC
NodeB
MS
Iub
HLR
SMSC
DNS
RADIUS
DHCP
Charging Centre
NMS / OSS
Service & subscriber management
PCRF
Gx/Gz
Gz/Gs/Gr/Gf/Gd
MGW
MSS/VLR
MGW
MSS/VLR
PSTN
Other PLMN
IuCS
Nb
A
Nc
Mc
Mc
Packet Core Domain
Circuit Core Domain

## Slide 8: Acronym in 2G / 3G
MS | Mobile Subscriber | A mobile phone with SIM card
BTS | Base Transceiver Station | Air interface toward MS in 2G
BSC | Base Station Controller | Controlling BTS
NodeB | n/a | Air interface toward MS in 3G
RNC | Radio Network Controller | Controlling NodeB
MSS | Mobile Switching Server | Mobility Management for CS Domain
VLR | Visitor Location Register | Manage temporary subscriber information within an MSS
HLR | Home Location Register | Manage permanent subscriber Database
MGW | Media Gateway | Manage user plane traffic
SGSN | Support GPRS Service Node | Mobility Management for PS Domain
GGSN | Gateway GPRS Service Node | Session Management , IP address allocation, QoS enforcement, Routing toward internet.

## Slide 9: A Simplified 2G/3G PS Call Flow…(1/3)
SGSN
GGSN
Packet Data Network
e..g Internet
Gn
Gb IuPS
BSC
RNC
BTS / Nodeb
MS
Abis / Iub
HLR
Gn DNS
Attach request..
Attach accepted..
Get info for this subscriber
Herewith the info
I am attached to the network and want to browse, by activating PDP context
Reference :
TS 23.060
TS 24.008
TS 29.060
Internet DNS
Note :
  All procedures here are simplified for overview only. Reader should refer to above reference for detail procedures.
1
2
3
4
5

## Slide 10: A Simplified 2G/3G PS Call Flow…(2/3)
SGSN
GGSN
Packet Data Network
e..g Internet
Gi
Gn
Gb -IuPS
BSC
RNC
BTS / Nodeb
MS
Abis - Iub
HLR
Gn DNS
PDP context activation received from MS,
What is the IP address of the GGSN that serving this APN ? ?
Herewith the IP address of GGSN
Create PDP Context Request
Create PDP Context accepted
Create PDP context accepted, send this info to MS
Reference :
TS 23.060
TS 24.008
TS 29.060
Internet DNS
Note :
  All procedures here are simplified for overview only. Reader should refer to above reference for detail procedures.
I am attached to the network and want to browse , by activating PDP context
5
6
7
8
9
10
PDP context activation accepted, now browse to
www.google.com.au
11

## Slide 11: A Simplified 2G/3G PS Call Flow…(3/3)
SGSN
GGSN
Packet Data Network
e..g Internet
Gi
Gn
Gb -IuPS
BSC
RNC
BTS / Nodeb
MS
Abis - Iub
HLR
Gn DNS
Reference :
TS 23.060
TS 24.008
TS 29.060
Internet DNS
Note :
  All procedures here are simplified for overview only. Reader should refer to above reference for detail procedures.
PDP context activation accepted, now browse to
www.google.com.au
11
12
13

## Slide 12: 4G Core
Protocol used in the control plane messaging has evolved.
  Changes in Transport Layer protocol while keeping all the Application Layer remain unchanged.
  Completely changed at Transport and Application Layer.
Transport Layer has changed dramatically from legacy protocol toward IP.

## Slide 13: General LTE Architecture
User plane
Control plane
SGSN
RNC
NodeB
S4
S12 DT
Iu
R8 3G
BSC
BTS
2G SGSN
Gb
R8 2G
Gn
Gn
BSC/RNC
Pre R8 2G/3G
SGSN
BTS/NodeB
Gb
Iu
R7 DT
PCRF
Gx
S1-MME
S1-U
S6a
HSS
eNodeB
S10
MME
LTE
S5
PGW
SGW
SGi
SGi
S11
S3
SGs
MSC
SGi
Internet
Operator services
Basic EPS architecture defined in 3GPP TS 23.401
Notes: S1-MME: C-plane between EUTRAN and MME
S1-U: U-plane between EUTRAN and Serving GW
S3: User & bearer information exchange for inter 3GPP access system mobility in idle and/or active state. It is based on Gn reference point as defined between SGSNs.
S4: U-plane with related ctrl. & mobility support between GPRS Core and 3GPP Anchor. It is based on Gn reference point as defined between SGSN and GGSN.
S5: U-plane tunneling between Serving and PDN GW. It is used for Serving GW relocation and in case Serving GW needs to connect to a non collocated PDN GW for the required PDN connectivity
S6a: Transfer of subscription & auth. data for authenticating/authorizing user access to EPC
S7: Transfer of policy & charging rules from PCRF to PCEF
S8a: inter PLMN variant of S5
S10: Reference point between MMEs in case of relocation and information exchange
S11: Reference point between MME and Serving GW
SGi: Reference point between PDN SAE-GW and packet data network. Corresponds to Gi/ Wi functionalities.
Rx+: Reference point between AF and PCRF based on current Rx (necessary modifications are FFS)

## Slide 14: Acronym used in 4G
E-NodeB |  | Air interface toward MS in 4G
MME | Mobility Management Entity | Mobility Management for 4G, Control Plane only
S-GW | Serving Gateway | Mobility Management for 4G for User Plane, Handover anchoring .
P-GW | Packet Data Network Gateway | Routing to Packet Data Network, Session Management, IP address Allocation. Function of P-GW is similar to GGSN in the 2G/3G network
HSS | Home Subscriber Server | Manage Permanent 4G subscriber data. Evolution of HLR.

## Slide 15: Thank You