## Slide 1: DASAR TELEKOMUNIKASI TCP/IP
Syarifah Muthia Putri, ST., MT

## Slide 2: OSI (Open Systems Interconnection)
ISO (International Standards Organization), 1947
OSI : Suatu model sistem interkoneksi hardware dan software yang membagi task (proses/tugas) kompleks menjadi subtask (subproses) dalam bentuk layers (lapis-lapis)
OSI model : 7 Layers
Layer yang lebih tinggi menggunakan services (layanan) layer di bawahnya

## Slide 3: Model OSI (7 layers)

## Slide 4: TCP/IP And OSI Model

## Slide 5: TCP/IP And OSI Model

## Slide 6: OSI Layers

## Slide 7: Exchange Using OSI Model

## Slide 8: Physical Layer
Physical Layer : Megirimkan bits antar nodes
Unit komunikasi : bit
Notes: Physical layer concerns: Physical characteristics of interfaces and media, Representation of bits, Data rate, Synchronization of bits, Line configuration, Physical topology, Transmission mode

## Slide 9: Data Link Layer
Data Link : Mengirimkan frame antar node
Unit komunikasi : frame
Defines frames into manageable data units, Physical addressing, Flow control, Error control, Access control

## Slide 10: Network Layer
Network Layer : Mengirimkan packet dari original source ke tujuan
Unit komunikasi : packet
Source-to-destination delivery, possibly across multiple networks
Logical addressing
Routing

## Slide 11: Transport Layer
Transport layer : mengirimkan pesan dari satu proses ke yang lainnya
Process-to-process delivery of entire message
Port addressing
Segmentation and reassembly
Connection control: connectionless or connection-oriented
End-to-end flow control
End-to-end error control

## Slide 12: Session Layer
Session Layer : responsible for dialog control and synchronization

## Slide 13: Presentation Layer
Presentation layer is responsible for translation, compression, and encryption.

## Slide 14: Application Layer
Application Layer : menyediakan layanan ke user
Enables user access to the network
User interfaces and support for services such as
  E-Mail, File transfer and access, Remote log-in, WWW

## Slide 15: Summary of Layers

## Slide 16: Addressing in TCP/IP

## Slide 17: Addressing in TCP/IP

## Slide 18: Addressing in TCP/IP : Physical
07:01:02:01:2C:4B
A 6-byte (12 hexadecimal digits) physical address.

## Slide 19: Addressing in TCP/IP : Network
132.24.75.9 An internet address in IPv4 in decimal numbers
80 A 16-bit port address represented as one single number.

## Slide 20: Terima Kasih
There is a sky beyond the sky